## Slide 1: Alex Kelly GE Digital

## Slide 2: A little more about me.
2013 – Bachelors of Science in Computer Science, Clemson

## Slide 3: 2011-2013, NYC – Berkshire Hathaway

## Slide 4: 2013-2015, Redmond - Microsoft
Power BI

## Slide 5: 2015-2017, Austin – GM
http://gm.com

## Slide 6: Current

## Slide 7
git clone https://github.com/pilotdeveloper/iot_lab.git
Mac users:
Try this solution:
https://medium.com/@tony92151/arduino-ch340-chip-driver-for-high-sierra-39e621dae1e4

## Slide 8: ENSURE YOUR BAG HAS
8 male to female jumper cables
10 male to male jumper cables
10 µf electrolytic capacitor
1x NRF24L01+ Transceiver
4 tactical buttons
Arduino
Breadboard
USB Cable

## Slide 9: Test your board
Open the Arduino IDE
Select Tools, Click Board -> Arduino Nano
Take note of the current devices under Tools -> Port (write down so you don’t select them later)
Plug your Arduino in, wait about 20 seconds, and then check under Tools -> Port.
      Windows – should show as a COM# device
      Mac Users – check the file called “mac_help.txt” in the repo.
Open the file helloworld/helloworld.ino and click the run button in Arduino

## Slide 10: hello_world.ino
Once you have hello_world running, you should be able to type a character and have your Arduino respond. If it doesn’t, please see me before we continue!

## Slide 11: Parts we’re using
NRF24L01+ Wireless Transceiver
Arduino Nano
10 µf Capacitor
Breadboard
Shoe Boxes

## Slide 12: How to connect the NRF24L01 to Arduino
NRF24L01+ | Arduino Pin
1 – GND | Ground
2 – VCC | 3v3
3 – CE | D9
4 – CSN | D10
5 – SCK | D13
6 – MOSI | D11
7 – MISO | D12
8 – IRQ | D8

## Slide 13: Capacitor
Bursting a signal requires a lot of energy – around 100 mA depending on the transmission strength. The Arduino Mano is not capable of handling this burst over 3.3v, so you have to add a capacitor to account for the voltage drops.
The capacitor must be connected across 3.3v and Ground on your NRF24L01. See photo in diagrams called “capacitor” for info on how to do this.
Be sure that the - - - (on the side of the capacitor) is on the ground side – you’ll short out the device if not!

## Slide 14: Tactical Switches

## Slide 15
Connect GND to the Negative Rail (Blue – on either side)
Press your buttons in to the bread board, ensure AB are on left & CD are on right
Connect the left side of the switches (A) to the Negative rail with four male to male jumper wires.
Connect the right side of the switch to D2, D3, D4, and D5 respectively
(see all images in github repository for additional info)

## Slide 16: Program your board
Open Transmitter.ino and set your group number equal to tableNumber.
Fix the code!
Add NRF24 to your dependencies before you compile!!!

## Slide 17: Connect with me!
https://ajkelly.net
https://linkedin.com/in/alexanderjkelly